## Slide 1
Silent & Accurate Stepper Motor Controller
Feedback
Systems
Control Algorithms
Applications
Lara et al. used linear search optimisation to improve performance of magnetic encoders
Dorin-Mirel et al. (2017) showed that closed loop control is more effective than open loop when operating stepper motors
Driving Motors
Step-out (slip) occurs when torque varies particularly at high speeds. Current not stable at high speeds (Le et al.)
Hardware
Software
Le et al. proposed a solution to produce maximum torque and recover step losses
Transport of fuel elements in nuclear engineering Dorin-Mirel et al.
Needs more precise control to reduce step losses
Voltage controlled chopper reduces the current fluctuations (Trinamic 2015)
Current controlled choppers cause fluctuating eddy currents in motor (Chen et al. 2014)
MATLAB and Simulink model set up by describing a motor with a set of equations. Mathematic (Oo 2017)
feedback loop needs to be introduced into control model
Hardware-in-the-loop not used to confirm simulation results
Modeling
Optical encoders are precise but are large (Fell 2014).
Voltage waveform analysis was not successful for detecting speed at low speeds Dorin-Mirel et al. (2017)
There is an effect on the noise of a stepper motor depending on the type of control curve (s-curve or trapezoidal) Zhang et al. (2017)
Algorithm can be improved to be more efficient
Dampening in the control loop controlled motors more efficiently.
Successfully developed silent motor driver based on a voltage controlled chopper design
Placing an inductor in series with each winding can reduce current ripple